## Slide 1: Zipit Bluetooth Serial mod. Steve Adolph
Goal: Enable portable internet connectivity for a Tandy 200 using a Zipit Z2
Tandy200 RS-232 bluetooth  Zipit Z2  internet
Approach: Add internal bluetooth serial adapter to the Zipit Z2
  Use RN-42 from Sparkfun: enables serial over bluetooth
  Tandy 200 has a matching bluetooth adapter
Minimal impact on look/feel of Zipit

## Slide 2: Internal Connections
RN-42: RS-232 + flow control
TxD, RxD, RTS, CTS, +3.3V, GND
Zipit Z2: ttyS1 is assigned to the “BT” serial port
3 signals on edge connector, 1 on PCB
(backside of Z2 LCD screen)
top
_________________________________________
| 36-pin connector . |
---------|_________________________________________|------- DC [O]
|||||||||||||||||| ||||||||||||||||||
bottom 36 19 18 1 (ext. +5VDC)
Connector Pin # Connected To Function Use
------------------------------------------------------------------
31 CPU C17 GPIO (45) BTRTS
36 CPU A20 GPIO (44) BTCTS
7 CPU D20 GPIO (42) BTRXD
- CPU B21 GPIO (43) BTTXD (connect at smd pad on board)

## Slide 3: Serial port connections
CTS
RTS
RxD
TxD

## Slide 4: Wired up
3.3V

## Slide 5: RN-42 placement

## Slide 6: Comments
RN-42 fits snugly in the lcd cover, and there is no height problem.
I notched the foam to make room for RN-42, ad the wires.
Soldering was very tricky. I used a microscope and a third hand vice.
Adding LEDs for status would be a possible also.